## Slide 1: Image Analysis and Processing with Image-J
Austin Blanco
2011

## Slide 2: Example Imaging Workflow
Acquire
Display
Lookup Tables
Scaling
Process
Kernels
Morphometry
Arithmetic
Segmentation (Thresholds)
Covered in Quantitative Imaging Fundamentals

## Slide 3: Processing Overview
Processing algorithms in microscopy:
  Affects on Data
  Filter Categories and Uses
  Parameter Control & Scripting

## Slide 4: How do filters affect data integrity?
Images are excel files.
Filters are mathematical calculations
  Given the same input the output never changes
  Output change amounts can be measurably determined (difference between raw & processed)

## Slide 5: Types of image processing
Kernel convolutions
Binary operations
Arithmetic operations
Morphological convolutions

## Slide 6: Kernel Convolution
-1
-1
-1
-1
9
-1
-1
-1
-1

## Slide 7: Try it out
Open supplied image “Shapes.tif”
Select Image ->Adjust -> Brightness/Contrast.
Scale to your preference
Select Process -> Filters ->
  Gaussian Radius 1, Preview on.
  Maximum, Preview on.

## Slide 8: Real World Use
Open “Smooth Example.tif”
Threshold the image
  Image -> Adjust -> Threshold
Run Gaussian Filter
Threshold the image.

## Slide 9: Why use Binaries?
Binaries:
  Allow regional processing within an image
  Support Multiple layer arithmetic operations
  Interact with regions for advanced measurement.
Examples
  Cut areas between two points
  Measure regions outside or inside of a definable boundary
  Analyze small objects (organelles/processes) within a larger object (cell).

## Slide 10: Binary Operations
“Intensity” Image
Intensity
X Axis in Image
“Binary” Image
Intensity
X Axis in Image

## Slide 11: Binary Operation Usage
Threshold Image
Run Filter
Analyze Result
Binary Reference
Advanced Count

## Slide 12: Try it out
Open “Simple Binary.tif”
Select Image -> Adjust ->Threshold
Set range to Min=0, Max=141, Click Apply
Select Image -> Duplicate
Select Process -> Binary -> Dilate (repeat 2x)
Select Process -> Image Calculator
  Select “Difference” Method and click Apply
Other Operations – AND/OR/SUB?

## Slide 13: Arithmetic Operations
Three methods
  All pixels in an image are calculated against a constant value (Process -> Math -> Subtract)
  Pixels from image A are calculated against image B.
  Pixels from images 1 to N in a stack are calculated against one another.

## Slide 14: Try it Out
Open “Math_YFP” and “Math_DAPI”
Threshold DAPI Image + apply
Multiply Dapi (Binary) Image
  (process ->math-> Multiply)
  Why is this required?
Process -> Image Calculator, AND.
Result = YFP Signal where Dapi Binary is Positive.

## Slide 15: Morphological Convolutions
Treat each brightness value as a separate binary layer. (eg intensity 0,1 – then intensity 1,2 from 0 to image maximum)
Uses Filters on whole image that used to be restricted to binaries.
Provides more utility without requiring moving image into binary space (saves time).

## Slide 16: Try it Out
Open “Morphology Example.tif”
Select Process -> Morphology -> Grey Morphology
  Note the following abilities which operate on an intensity image:
      Erode
      Dilate
      Open
      Close

## Slide 17: Processing Workflow Options
Original Image
Processing used to identify objects
Measurements taken and processing changes accepted.
Original data is re-applied
Processing only used for segmentation
Measurements taken only on original data areas
Faster
More Accurate

## Slide 18: Q & A

## Slide 19: Example Imaging Workflow
Acquire
Display
Lookup Tables
Scaling
Process
Kernels
Morphometry
Arithmetic
Segmentation (Thresholds)
Analyze
Area Analysis
Object Analysis
ND Analysis
Advanced Analytics

## Slide 20: Area Measurements
Whole Image
User Defined
  Regions
  Threshold

## Slide 21: Try it Out
Open “Mch_488.tif”
Draw a region
Select Analyze -> Measure.
  Repeat measurements using CTRL+M
  Select Process -> Analyze -> Tools -> ROI Manager.
  Move region, click ADD
  Repeat a few times, then click Measure.
  ***Note Click+Drag Still Functional

## Slide 22: More Area Measurements
Select File -> Open Samples -> MRI Stack.
Draw a new region
Select or open ROI Manager
  Clear Old Measurements.
  Add New Region
  Select “More” – “Multi-Measure”.
  Click OK.

## Slide 23: Object Measurements
  What is a “Morphometric Object”?
    Group of connected pixels
    Pixels are thresholded as signal
    Morphometry measurements (used to classify cells/objects etc) can be performed on groups, or objects.
Identified Object

## Slide 24: Object Measurements
Width
Length
Perimeter

## Slide 25: Problems
“Length”
“Area”

## Slide 26: Try it Out
Open “Mch_420.tif”
Threshold Image
  Select Analysis -> Set Measurements
  Note # of Measurements / Options available
  Select Analysis -> Analyze Particles.

## Slide 27: Analysis Window
Object Inclusion
Overwrites original image, when applicable
How to view Detected Particles

## Slide 28: Putting it All Together
Example of using Threshold, Binary, Math and Particle Analysis.
Step 1 – Segment Objects for Clean Count.
  Clear All Windows, Re-Open “Mch_420.tif”
  Select Edit-> Duplicate. Work on 420-1.
  Open Threshold -> Apply.
  Select Binary -> Watershed.
  Select Binary -> Erode.
  ***Good Segmented Binary Image is now Complete.

## Slide 29: Putting it All Together
Step 2 – Apply Segment to Original image.
  Activate Binary Image (click on it)
  Select Image -> Type -> 16 Bit.
  Select Process -> Math -> Multiply (255)
  Select Edit -> Invert.
    Reference is Ready for Calculation.
  Select Process -> Image Calculator
    Set Ref A= Mch_420 (Original) and Ref B = Mch_420_1
    Calculation = Subtract -> Check “New Window” –Apply

## Slide 30: Result

## Slide 31: Putting it All Together
Step 3 – Analyze Image
  Threshold Image (DO NOT Click “Apply)
  Select Analyze Particles
  Set Minimum object area to 400.

## Slide 32: Thank You